## Slide 1: OMC-048 Training
This subject is NOT about the OMC-048!
A terminal program changes your computer into a dumb terminal (keyboard + display)
COM port (often USB<>COM)
RS232/(422)
Tx/(TxA, TxB)
Rx/(RxA, RxB)
Sensor,
logger,
…
Tx
Rx
Tx = Transmit (Output)
Rx = Receive (Input)
Terminal programs and COM ports

## Slide 2: OMC-048 Training
Windows key + X => Device manager (apparaatbeheer)
Terminal programs and COM ports

## Slide 3: OMC-048 Training
Terminal window, or ‘REPL’
USB/REPL/SD
FLASH drive with ‘config.txt’ file
32 GB SD drive with ‘data’ and ‘script’ and ‘system’ folders.
Will NOT appear in ‘REPL’ mode!

## Slide 4: OMC-048 Training
Generic drivers & reference tables
The ‘config.txt’ file tells the logger which sensors/peripherals are connected, and what to do with them
Input drivers
Sensors and other ‘data sources’
Output drivers
Cellular or satellite communication, or ‘generic serial’ output.
Generic drivers & reference tables.
These require ‘customization’

## Slide 5: OMC-048 Training
Hint: Formulate like this!
Timing Specification
Interval : “0,20,40 * * * *”
On second 0, 20 and 40 of every minute of …. etc.
Answers
“0 0,20,40 * * *”
“5,35 * * * *”
“50 59 * * *”
Exercise: write timing specification for:
Every 20 minutes (00:00:00, 00:20:00, 00:40:00, ….
Every 30 seconds at 5 s past the(half) minute (00:00:05, 00:00:35, ….)
Ten seconds before every whole hour.
Next click shows the answers!
Interval : “s m h d w”
On second s of minute m of hour h of day d (1-31) of weekday w (1=Monday)
Format:
Meaning:
Interval : “0 10 * * *”
On second 0 of minute 10 of every hour …. etc.
Examples:
Meaning:
Interval : “* * * * *”
On every second of every minute of every hour of every day of every weekday
Use ‘*’ to indicate ‘every’

## Slide 6: OMC-048 Training
Data files explained
OMC-045_training_048000125_220110_120110
File format (is NOT logger type)
In config.txt: “system_id: training”
Serial number
Date
Time
Date&time of file creation (open)
File name:
Files are stored on SD and transmitted by FTP